## Slide 1
BTP / AUTONOMOUS DRIVING
From inherited baseline to a multimodal driving policy
Literature → implementation → evaluation plan
RGB cameras · LiDAR BEV · speech · PPO
Research & implementation review
01

## Slide 2
01 · STARTING POINT
What the project inherited
02
• Semantic-segmentation ground truth was used as the perception input.
• A VAE-based pipeline carried a large model footprint and high latency.
• Training and evaluation on the same town did not test cross-map generalization.
• Speech interaction existed separately from the driving loop.
Legacy MTP
Segmentation
VAE
Town02 → Town02
The redesign starts by removing these assumptions.

## Slide 3
02 · DESIGN
The system I am building
03
3 × RGB
LMDrive
BEV LiDAR
TransFuser
Speech
wav2vec 2.0
Kinematics
state
Multimodal encoder 128-d latent
+ 5 kinematic values → 133-d state
PPO actor–critic
speech intent conditions the representation rather than blocking the control loop

## Slide 4
03 · LITERATURE
The papers are used for specific decisions
04
LMDrive
camera layout; auxiliary pre-training
TransFuser
BEV LiDAR representation
wav2vec 2.0
speech feature extraction
FiLM
feature-wise language conditioning
MobileNets
depthwise-separable convolutions
CAPS
action smoothing
CaRL + Roach
PPO / CARLA training
Talk2Car
language-conditioned driving
BEVDet
shared-weight multi-camera encoding
DriveVLM + EMMA
architectural context
CAPS replaces PINNsformer in the current literature audit.

## Slide 5
04 · ENCODER
A small multimodal encoder, not a large VLM
05
RGB / BEV inputs
Shared-weight patch embeddings
FiLM conditioning 8 speech intents
2-layer Transformer
Global average pooling → 128-d
Implementation targets
• 800 tokens · d = 64
• 133K parameters
• ≈ 0.51 MB model footprint
The point is to keep the representation small enough for edge deployment.

## Slide 6
05 · SENSORS
What enters the encoder
06
LEFT RGB −60°
FRONT RGB 0°
RIGHT RGB +60°
LiDAR → BEV
shared-weight visual encoding
Speech intent
FiLM
128-d latent
Kinematics are appended after the visual-language representation.

## Slide 7
06 · SPEECH
Speech is a control signal, not another camera
07
16 kHz audio
wav2vec 2.0
8 driving intents
FiLM → visual features
Example command flow
“turn left” → intent → conditioning → state → PPO action
Sparse spoken commands can update the state without waiting on the 20 Hz control loop.

## Slide 8
07 · DATA
Training data is deliberately separated by town
08
Town01
20K synchronized frames
Pre-train encoder
→
PPO training
1M timesteps (target)
Closed-loop control
→
Town02
50 evaluation episodes
No fine-tuning
Town01 → Town02 is the generalization test; success should only be claimed after the run.

## Slide 9
08 · PRE-TRAINING
Before PPO, teach the encoder basic vehicle state
09
RGB + LiDAR + speech
Multimodal encoder
128-d latent
steering prediction MSE
speed prediction MSE
Auxiliary losses
The roadmap uses 40 epochs for steering + speed pre-training before PPO.

## Slide 10
09 · CONTROL
PPO sees a compact state
10
128-d multimodal latent
+ 5 kinematic values
133-d state
→
PPO actor–critic 500 → 300 → 100
steering + throttle
Action smoothing is treated separately from perception; CAPS is the literature reference here.

## Slide 11
10 · EVALUATION
What needs to be measured
11
Route completion
Town02
Collision rate
Town02
Average speed
Town02
Command adherence
Speech
Inference latency
RPi 4
Throughput
FPS
Memory footprint
MB
Measured values belong here once those runs exist.

## Slide 12
11 · EDGE TARGET
The benchmark is a gate, not a result
12
≤ 25 ms
latency target
> 40 FPS
throughput target
≤ 1.5 MB
memory target
Physical test
Raspberry Pi 4 · 500 inference cycles · CPU benchmark
Only after this run should the deck claim an edge-latency improvement.

## Slide 13
12 · TRACEABILITY
Literature → implementation
13
LMDrive
→
camera placement + auxiliary pre-training
TransFuser
→
LiDAR → BEV
wav2vec 2.0
→
speech representation
FiLM
→
speech → feature modulation
MobileNets
→
efficient visual blocks
CAPS
→
smooth actions
CaRL / Roach
→
CARLA PPO training
This is the slide to defend when someone asks: “Why this component?”

## Slide 14
13 · ROADMAP
What happens next
14
1
Redesign
sensor + encoder
→
2
Data
Town01 / 20K
→
3
Pre-train
steer + speed
→
4
PPO
closed loop
→
5
Generalize
Town02 / 50 eps
→
6
Edge
RPi 4
→
7
Write-up
report + defense
Distinguish completed work from targets throughout.
No “project complete” claim until the evaluation evidence exists.

## Slide 15
14 · DELIVERABLES
What the final evidence should contain
15
• Architecture: sensor-to-policy diagram and implementation details.
• Literature: paper → design-decision mapping.
• Data: Town01 collection and training split.
• Evaluation: Town02 generalization curves and collision / completion metrics.
• Edge: Raspberry Pi latency, throughput and memory measurements.
• Reproducibility: scripts, checkpoints and result files.
The final story is evidence-led: what changed → why → how → what happened.

## Slide 16
BTP / NEXT CHECKPOINT
Build it. Measure it. Then make the claim.
Town01 → PPO → Town02 → Raspberry Pi
The deck is written around the work itself, not around presentation templates.
Sources and paper details can sit in speaker notes / reference appendix.
16